## Slide 1: NTSB Narrative Project — Full Story

## Slide 2: Today's map (15 min)
Where we started: Zhang's network + your structural-mapping idea
Dead end #1: LLM computes probabilities directly
What we built: LLM reads → frozen network calculates
Proof: reproduce Zhang + 296 held-out accidents (~91% injury, leak-safe)
Your idea tested exhaustively → appendix negative result
Notes: One arc: reproduce calculator, narrative bridge, fair test of struct mapping.

## Slide 3: The one picture: build time vs query time
BUILD (once): coded data → frozen BN; narratives → embedding index
QUERY: counting path (one condition) OR network path (many facts)
Rule: narrative never retrains the network
The LLM is the reader. The network is the calculator.
Notes: Undergrad analogy: calculator trained on old accidents, frozen; new stories only fill in the form.

## Slide 4: Dead end #1: LLM-only probabilities
Asked GPT for probabilities directly → ~10x wrong vs Zhang
One word change → different answer (not reproducible)
Lesson: LLM = translator; network = calculator
Notes: This motivates Section 3.5 / tiered parser design.

## Slide 5: Reproduction: what we fixed before trusting narratives
Issue | Fix | Result
Fire count 38→102 | Merge occurrence files | Denom 102 ✓
Table 7 partial | Cause/Factor filter | 85/85 exact
No pilot nodes | Person findings | Fig 12 runs
Boolean injury | 4-level severity | Held-out eval
Trust the calculator first, then test narratives.
Notes: Table 7 85/85; scoreboard 77/93 after upgrades.

## Slide 6: Final pipeline: tiered parser → evidence → frozen BN
Tier 1: NTSB vocabulary match (11/11 scenarios; 10/11 no LLM)
Tier 2: LLM only when Tier 1 empty; strengths from data
Hard + soft + stated evidence → propagation
Notes: outputs/combined_parser_validation.md

## Slide 7: Does it work? 296 held-out accidents (2007–2019)
Method | Injury | Damage
Prior (no narrative) | 58.4% | 42.6%
Event evidence → frozen BN | 89.9% | 55.7%
k-NN severity via frozen BN (primary) | 90.9% | 77.4%
Supervised LR (parsed features) | 87.8% | 64.2%
Supervised LR (narrative embedding) | 91.6% | 74.0%
Narratives early; coded labels late — ~91% injury on unseen cases, zero trained parameters, leak-audited.
Notes: Never used in network construction. Leak-safe: outcome phrases redacted before embedding; stated-severity readout OFF (supersedes pre-audit 93%/81%). Source: outputs/heldout_significance.md

## Slide 8: Your idea: structural mapping
LLM extracts causal chain (role / system / mechanism steps)
Align chains (Needleman-Wunsch); rerank by structure + cosine
Goal: find 'same mechanism, different words' cases cosine misses
Notes: Frame as reasonable hypothesis we tested to falsify properly.

## Slide 9: Structural mapping: every variant we tested
Variant | What it tests
A0 embedding baseline | Cosine similarity only
A2 rerank top-50 | Your original rerank idea
V1 best-match bypass | Drop cluster averaging
V3 wider pool rerank | Change pool then rerank
V4 struct-first ALL 1,703 | Retrieve by structure alone
V5 hybrid embedding | Narrative ⊕ chain in one vector
V6 struct severity vote | Structure on 296 held-out task
Rerank, replace retrieval, hybrid — every insertion point.
Notes: outputs/structmap_final_verdict/REPORT.md

## Slide 10: Structural mapping: results
Test | Result
Rerank A2 vs A0 (diagnosis) | No significant win
V1 best-match bypass | Harmful −1.6 to −2.6 pp (p<0.001)
V4 struct-first (severity) | Injury 92.9%→81.1%; damage 81.4%→70.9%
Best struct cell (1 of 28) | +1.4 pp damage, p=0.125 (noise)
k=50 no structure control | +1.0 pp damage (same noise)
Exhaustively null. Best struct win = pool-size jitter.
Notes: Never beat baseline; struct-first hurts severity. Severity rows were run PRE-redaction (baseline 92.9%/81.4%); paired comparison still valid — every variant saw the same text.

## Slide 11: Why structural mapping did not help
Chains too generic (~5 steps) — many accidents share the same shape
Embedding already encodes most signal (struct ρ ≈ 0.01 vs truth)
When struct disagrees with embedding, it is wrong more than right
Averaging 50 neighbors beats picking one 'best struct' incident
Notes: Honest to Jesse: idea testable; this extraction stack is information-poor.

## Slide 12: Where we are + question for you
Paper: reproduce Zhang + narrative bridge + held-out 296 + ablations
Struct mapping → Appendix A (clean negative result)
OK to freeze struct mapping as closed?
Anything you want rerun before we finalize the draft?
Notes: Stop and let Jesse direct.