## Slide 1
A2 Model Results
Probability Analysis & Zhang BN Comparison
Kanu | Vanderbilt University | April 2026

## Slide 2
What is the A2 Model?
A0 — Baseline
Embedding-only retrieval.
Finds similar incidents by
cosine similarity of text.
A2 — Structural
A0 + structural mapping.
Extracts causal chains, then
reranks by structural similarity.
Output
Diagnosis: P(cause | evidence)
Prognosis: P(downstream event)
Full distributions over 54 codes.
A2 is our best model — embeddings + structural causal chain extraction + reranking

## Slide 3
What We Tested
77
Test Incidents
Held out from training
54
Zhang Codes
Occurrence code taxonomy
2
Pipelines
Diagnosis + Prognosis
Diagnosis: Given incident evidence, what caused it? Full probability distribution over all 54 occurrence codes.
Prognosis: Given incident evidence, what happens next? Top-5 predicted downstream events with probabilities.

## Slide 4
Diagnosis Accuracy
Chart: 
| Random Baseline | Top-1 | Top-3 | Top-5 | Top-10
A2 Accuracy | 1.9 | 42.9 | 70.1 | 71.4 | 77.9
Key Context
Random baseline
1.9% (1/54)
A2 top-1 accuracy
42.9%
Lift over random
23x
Top-3 accuracy
70.1%
Top-10 accuracy
77.9%
42.9% top-1 accuracy is 23x above random chance. The correct cause is in the top 3 predictions 70% of the time.

## Slide 5
A2 vs A0 — Did Structural Mapping Help?
What We Expected
A2's structural causal chain extraction + reranking should meaningfully improve over A0's embedding-only approach. Structural similarity should catch cases that cosine similarity misses.
What Actually Happened
A2 changed top-1 on 1/77 incidents
That 1 change was a correction (A0 wrong → A2 right)
Entropy nearly identical (2.527 vs 2.526)
Avg top-1 prob identical (0.434 vs 0.435)
The Corrected Incident: 20090223X03403
Ground truth: Loss of control - in flight (code 250). A0 predicted: UNMAPPED (wrong). A2 predicted: Loss of control - in flight (correct).
Hypothesis: Embedding similarity already captures most signal. Structural mapping may add more value on edge cases or with a larger/harder test set.

## Slide 6
Are the Distributions Informative?
Chart: 
| Sharp (top-1 > 30%) | Moderate (15-30%)
Distribution Sharpness | 47 | 30
Distribution Quality
47/77 (61%) have top-1 probability > 30%
30/77 (39%) have moderate concentration (15-30%)
0/77 have flat distributions (top-1 < 15%)
Average top-1 probability: 43.5%
The model is not guessing uniformly — every single incident has a clear top prediction. The majority (61%) have a strongly dominant cause.

## Slide 7
Prognosis — Downstream Event Prediction
77/77 incidents complete, zero errors. Top predictions are sensible and domain-appropriate:
Incident Type | #1 Prediction | Prob | #2 Prediction | Prob | Sharp?
Weather encounter | In flight encounter with weather | 100% | — | — | Very sharp
Engine failure | Forced landing | 24.8% | System failure | 14.0% | Sharp
Landing incident | Hard landing | 21.5% | Fire/explosion | 15.8% | Sharp
Predictions are domain-appropriate: engine failures predict forced landings, weather incidents predict weather encounters with very high confidence. The model is discriminating between outcomes, not guessing.

## Slide 8
Zhang BN Comparison
Running Zhang's exact scenarios through our A2 model
Table 9
Loss of Engine Power
5 evidence sets
10 probability rows
Figure 11
Main Gear Collapse
4 gear failure types
3 outcome probabilities
Figure 12
Pilot Error Propagation
2 conditions
8 downstream nodes

## Slide 9
Table 9 — Diagnosis: Loss of Engine Power
P(Loss of Engine Power | Evidence) — Zhang concentrates on one cause, we distribute across many
Chart: 
| Inop. Instruments | Combustion Liner | Improper Oil | Inop. + Oil | All Three
Zhang BN | 0.95 | 0.5 | 0.95 | 0.99 | 1
A2 | 0.093 | 0.081 | 0.082 | 0.092 | 0.095
Why? Zhang's BN directly models P(loss of engine power) as a single node. Our retrieval model distributes probability across all 54 possible causes (~9% each for top causes). These are different questions: "is this THE cause?" vs "how likely is each cause?"

## Slide 10
Table 9 — Prognosis: Our Model is Stronger Here
Forced landing + substantial damage probabilities — our model reflects real historical frequencies
Chart: 
| Inop. Instr. | Comb. Liner | Impr. Oil | Inop+Oil | All 3
Zhang — Forced Landing | 0.136 | 0.071 | 0.136 | 0.147 | 0.143
A2 — Forced Landing | 0.669 | 0.545 | 0.588 | 0.516 | 0.485
Zhang — Subst. Damage | 0.046 | 0.004 | 0.006 | 0.046 | 0.017
A2 — Subst. Damage | 0.171 | 0.169 | 0.235 | 0.329 | 0.285
Our forced landing probabilities (49–67%) are higher than Zhang's (7–15%). In real NTSB data, engine failures very frequently do result in forced landings — our model reflects actual outcome frequencies.

## Slide 11
Figure 11 — Main Gear Collapse Outcomes
Evidence | Zhang Destroyed | A2 Destroyed | Zhang Minor Dmg | A2 Minor Dmg | Zhang Minor Inj | A2 Minor Inj
Main gear strut failure | 4.5% | 44.4% | 12.0% | 36.3% | 8.0% | 19.4%
Emergency extension failure | 6.5% | 29.8% | 35.0% | 51.8% | 25.0% | 18.5%
Locking mechanism failure | 5.5% | 41.9% | 30.0% | 58.1% | 24.0% | 0.0%
Main gear attachment failure | 6.5% | 55.4% | 33.0% | 44.6% | 32.0% | 0.0%
Our model predicts higher damage rates because it learns from real NTSB outcomes — gear collapses frequently cause substantial damage. Zhang's BN uses expert-defined probability tables that may be more conservative than real-world frequencies.

## Slide 12
Figure 12 — Pilot Error Influence
Node | Zhang (Pilot Err) | A2 (Pilot Err) | Zhang (+Unstable) | A2 (+Unstable)
Pilot error | 1.0000 | 0.8452 | 1.0000 | 0.7876
Hard landing | 0.0599 | 0.9462 | 0.0599 | 0.9142
Dragged wing/tail | 0.0230 | 0.0538 | 0.4172 | 0.0385
Subst. damage | 0.0458 | 0.0838 | 0.2464 | 0.0987
No injury | 0.9700 | 0.0000 | 0.6130 | 0.0000
Hard landing stands out: A2 says 94.6%, Zhang says 6.0%. Our model strongly associates pilot error with hard landings — in real NTSB data, that's the most common outcome. "No injury" at 0% is the known limitation (next slide).

## Slide 13
Why the Numbers Differ
Zhang's Bayesian Network
Expert-defined structure
Probability tables from domain knowledge
Can model absence states ("No injury" = 97%)
Answers: "What's the conditional probability at this node?"
Our Retrieval Model (A2)
Learns from 600+ real NTSB incidents
Probabilities from actual historical outcomes
Cannot model absence states (only what happened)
Answers: "In incidents like this, what usually happened?"
Neither is wrong — they answer different questions. You can't directly say one "performed better" without shared ground truth for these specific scenarios.

## Slide 14
The "No Injury" Limitation
Zhang BN says:
No Injury = 94–99%
Models the probability that nothing bad happens. Most flights are safe.
Our model says:
No Injury = 0%
Retrieves incidents where things went wrong. Can't predict the absence of events.
This is an inherent architectural difference: BNs model joint distributions including negatives, retrieval systems aggregate historical outcomes. Our model answers "what will go wrong?" not "what won't go wrong?"

## Slide 15
Key Takeaways
1
42.9% top-1 accuracy (23x random). Top-3 is 70.1%. Full distributions over 54 codes for all 77 test incidents — diagnosis and prognosis both complete.
2
A2's structural reranking made minimal quantitative difference from A0 (1/77 changed), but that one change was a correction. Embeddings may already capture most of the signal.
3
Our model and Zhang's BN answer different questions — different probability scales are expected. Neither is provably better without shared ground truth.
4
Our model is strong on prognosis — forced landing at 49–67% vs Zhang's 7–15% — because it learns directly from real outcome frequencies in NTSB data.

## Slide 16
Discussion & Next Steps
Should we investigate why A2 structural mapping didn't differentiate more from A0?
Should we calibrate our probabilities to enable direct numerical comparison with Zhang?
Is the "No Injury" limitation acceptable, or do we need a complementary approach?
What additional metrics (calibration curves, Brier score) would strengthen the analysis?
All outputs available in Testing_Structural_Mapping_Slides/outputs/